## Slide 1: ANESTHESIA PART II

## Slide 2: Anesthesia Concepts
Assessment
Monitoring Devices
Thermoregulatory Devices
Intravenous Access
Positioning

## Slide 3: Assessment (Preoperative Evaluation)
Conducted by CRNA or Anesthesiologist
Necessary to gather information that may affect the patient’s anesthesia
past medical/surgical history
current medical/physical status
current surgical disease
medications currently taking
allergies

## Slide 4: Monitoring Devices
The patient is physiologically monitored continuously from prior to induction (initiation of anesthesia), during anesthesia (intra-operatively), until after anesthesia is completed after discharged from PACU

## Slide 5: Monitoring Devices (Types)
ECK/EKG (electrocardiogram)
Part of anesthesia machine
Noninvasive
Monitors electrical activity of the
patient’s heart and heart rate
Monitoring of heart function is critical
during anesthesia
Problems can be caught immediately
and corrected by the administration of
drugs by the CRNA or anesthesiologist

## Slide 6: Monitoring Devices (Types)
Blood Pressure Monitoring
Part of anesthesia machine
Noninvasive (with cuff) set at 3-5 minute intervals for monitoring
Invasive (with arterial line placement) gives continuous monitoring
Provides circulatory status of heart and vascular system
Allows for immediate treatment should problems arise by CRNA or anesthesiologist
Notes: Tx. Can be trendelenberg with hypotention or if hypotention is due to blood volume loss may need to give IV fluids or blood products, also give drugs if needed

## Slide 7: Monitoring Devices (Types)
Arterial and Venous Catheters
Pulmonary artery catheter
Central venous catheter
Together are called a Swan Ganz Catheter
Monitor heart function and fluid status of the patient

## Slide 8: Monitoring Devices (Types)
Temperature Monitoring
Part of anesthesia machine
Noninvasive (a small adhesive sticker applied to the patient’s forehead)
Invasive (esophageal, bladder, rectal) these are hooked up to a monitoring device that reads temperature continuously
Notes: Invasive techniques are most desirable as they are most accurate. For short procedures the noninvasive method will be employed

## Slide 9: Monitoring Devices (Types)
Pulse Oximetry (pulse ox)
Part of anesthesia machine
Noninvasive (can be applied to the finger, toe, earlobe, or across the bridge of the nose)
Provides continuous monitoring of the amount of oxygen saturation contained in the patient’s arterial blood
Works by light wave absorption/nail polish must be removed at site of placement
Notes: There are acetone pads similar to the alcohol pads that can be used to remove nail polish if it has not been done by the patient or those in preop holding

## Slide 10: Monitoring Devices (Types)
SARA (System for Anesthetic and
Respiratory Status)
Is part of the anesthesia machine
Capable of monitoring respiratory status and anesthetic gas levels provided to the patient
Components include:
- Capnography - Oxygen Analysis
- Spirometry
Notes: Define components See pg. 173 Caruthers

## Slide 11: Monitoring Devices (Types)
Stethoscope
Used with placement of the endotracheal (ET) tube
Will hear breath sounds clearly with the delivery of oxygen into the ET tube with correct placement
Can use in placement of nasogastric (NG) tube
Notes: Explain difference between the two

## Slide 12: Doppler
Ultrasonic device
Identifies and assesses vascular status of peripheral vasculature
Probe is sterile or is draped with a probe cover
Ultrasound box usually handled/controlled by anesthesia provider or circulator

## Slide 13: Monitoring Devices (Types)
Peripheral Nerve Stimulator
This is a battery operated device used to assess the level of neuromuscular blockade for those patients receiving neuromuscular blockers
Pressed against a nerve area (usually the ulnar or facial nerves) it will generate a series of one to four twitches from the patient (called train of four)
One to four twitches lets the CRNA or anesthesiologist know this patient is muscle relaxed (paralyzed) at a given level
No response indicates that the patient has received a maximal dose and must wait until return of @ least 1 twitch in order to “reverse” the pt’s muscle relaxant
Notes: Ask mike about this. Is it the thing they use against the temporal area?

## Slide 14: Monitoring Devices (Types)
Arterial Blood Gases (Arterial line)
Art line placement into the radial artery allows for the ability to draw off oxygenated blood (is from an artery) for assessment of the patient’s pH, electrolytes, oxygen content, and carbon dioxide content of the blood
Is crucial for prompt treatment of problems as seen with lengthy or complex surgeries
Notes: This blood, the oxygenated blood should be near perfect at all times. Problems can be corrected

## Slide 15: Thermoregulatory Devices (Hypothermia)
Post-operative hypothermia occurs when the patient’s temperature is less than 36° C or 96.8°F
60% of patients coming to PACU are hypothermic
Hypothermia causes delayed recovery time and is thought to possibly contribute to postoperative illnesses or complications
Shivering increases oxygen demands of the patient

## Slide 16: Thermoregulatory Devices
The OR is generally a cool environment
Temperature of the room is often set to allow for the comfort of the scrub team
Patients under general anesthesia do not produce heat. They rely on OR staff to keep their temperature normal
Simple measures such as providing warm blankets on the bed before the patient is transferred to it as well as applying warm blankets on top of the patient after they are transferred can help. Doing the same when surgery is complete can also be helpful.

## Slide 17: Thermoregulatory Devices
Applying an insulated bonnet to the patient’s head for the duration of surgery can help hold in body heat
Using warming blankets or Bair Huggers are most beneficial when their use is practical
Fluid warmers are also available to warm intravenous fluids as they are being administered

## Slide 18: Thermoregulatory Devices (Hyperthermia)
May be an indication of infection
May be an indication of malignant hyperthermia
Early recognition of the cause is vital to allow the patient to have the best outcome
Notes: Will talk about MH later

## Slide 19: Intravenous Access
It is crucial that IV access be provided for the patient undergoing surgery
IV access 1˚done through a peripheral vein site such as the arms
IV access can be through the legs or neck (preferable) if there are no viable arm veins
Central line access, through the subclavian vein can also be used

## Slide 20: Intravenous Access
IV access provides a way to rapidly treat a patient with medications should there be a problem during the course of the surgery
IV access is necessary for the administration of anesthetic agents, IV fluids, IV medications non-anesthesia related, and blood products
Notes: IV fluids for hydration

## Slide 21: Positioning
From an anesthesia perspective, positioning must allow for quick access to the patient’s airway as well as their IV sites
For a patient receiving general anesthesia, the patient must be supine to be intubated
For a patient who will be placed in a prone position for surgery, intubation takes place on the stretcher before transported to the OR bed
For patients placed in a lateral position for surgery, intubation takes place on the OR bed, then the patient is flipped on their side by OR staff

## Slide 22: Positioning
DO NOT MOVE a patient without getting the OKAY to do so from anesthesia
You would not want to be responsible for pulling out an IV or endotracheal tube!

## Slide 23: Anesthesia Administration
Selection
Preoperative medications
Methods of administration

## Slide 24: Selection
The type of anesthetic to be used is determined by the patient, surgeon, and anesthesiologist or CRNA
Patient: rapid-acting, reversed easily, and provides for analgesia (no pain) during the course of the surgical procedure as well as into the postoperative period (IDEALLY)
Surgeon: provides for good relaxation of the muscles, limits patient movement, and has few side effects for the patient

## Slide 25: Selection Continued
Anesthesiologist/CRNA: Allows for high percentages of oxygen to be used and is safe, leaving the body unaffected, as well as has a low level of toxic effects

## Slide 26: Preoperative Medications
Purpose of:
Relieve preoperative anxiety
Produce amnesia related to the surgical events
Decrease secretions of the respiratory tract to prevent aspiration of respiratory secretions
Prevent nausea and vomiting to prevent aspiration of gastric contents
Minimize pain
Aide in a smooth induction of anesthesia

## Slide 27: Preoperative Medications
Selection of:
Made by anesthesiologist/CRNA (preference)
Assess patient’s:
physical status
emotional status
age
weight
concomitant diseases
how much relaxation is needed

## Slide 28: Preoperative Medications
Classification of:
Sedatives and Tranquilizers
-reduce anxiety
-provide sedation and drowsiness
-have an antiemetic effect (prevent nausea
and vomiting)
-do not prevent pain
-provide amnesia
Notes: Ex. Valium and versed reduce anxiety, provide sedation. Phenergan, Visteril, and Inapsine minimize n and v

## Slide 29: Preoperative Medications
Narcotic Analgesics
Reduce pain perception
Raise pain threshold
Decrease amount of anesthetics needed during the surgical procedure
Examples are morphine, fentanyl (sublimaze), sufenta
Side effects include respiratory depression, nausea, vomiting, urinary retention, and capable of causing dependence with long term use
Notes: Fentanyl is DOC r/t it is fast acting, and has a shorter duration than the other two

## Slide 30: Preoperative Medications
Non-narcotic Analgesic
Reduces pain perception
Raises pain threshold
TORODOL

## Slide 31: Preoperative Medications
Anticholinergics (antimuscarinic)
PSNS depressant
Prevent mucous secretions in the mouth, respiratory tract, and digestive tract preventing aspiration of secretions by the patient during surgery
Are bronchodilators (increase heart rate and respiratory rate
Do not affect blood pressure
Antiemetic effect as well
Notes: Ex. Include atropine, Robinul, and scopolamine. Are ususally given as an adjuct to anesthesia instead of as a preoperative med r/t can cause excitement, and hallucinations

## Slide 32: Spinal Meds
When giving a spinal (or epidural), the medication that is given is broken down into three categories:
Hyperbaric - solution tends to settle towards gravity (sinks)
Hypobaric - solution tends to resist gravity (floats up)
Isobaric - solution neither floats or falls (stays where it is placed)
Reading this, you might think that the breakdown of the words would lead a hyperbaric solution to float up (hyper meaning above). The term “hyper” refers to the weight of the medication vs. the specific gravity of the CSF it is being injected to. “Hyper” in this sense means that the med is heavier (weighs more, or above) than the weight of the CSF it is injected in, making it fall. The opposite is true for hypo. It is lighter, so it floats up.
The issue here is what position you have your patient in when you administer a med. If the patient is in reverse trendelenburg position and you give them a hypobaric med, it might float up towards the head and knock out the ability of that patient to breath.

## Slide 33: Potential Complications of Anesthesia
Nerve injury from improper positioning
Shock
Cerebral vascular incident (stroke)
Convulsions
Delirium
Cardiac Arrest
Malignant Hyperthermia
Excitement
Respiratory obstruction
Bronchospam or laryngospasm
Vomiting and aspiration
Damage to dentition
Corneal abrasion
Drug or blood transfusion reaction
Hypothermia
Fluid & electrolyte imbalance

## Slide 34: Assisting During Anesthesia Administration
Preoperative Visits
Preoperative Routines
Post Anesthesia Care

## Slide 35: Preoperative Visits
For major surgeries, the CRNA or anesthesiologist may visit the patient the night before surgery if the patient is in the hospital
Routinely, patient is visited in the preoperative holding area before surgery by the CRNA or anesthesiologist and the circulator
The patient is interviewed, assessed, provided emotional support, and educated
Notes: The surgeon may visit in preop and will if requested to

## Slide 36: Preoperative Routine
CRNA/Anesthesiologist
May assist with transport to the OR
Applies monitoring devices
Prepares for induction
Surgeon
Available if needed
Notes: Remind there are other personnel involved ex. Anesthesia techs, NAs to assist with anesthesia and positioning

## Slide 37: Preoperative Routine
Circulator
Transports to OR
Assists with transfer to OR bed
Applies safety strap and provides comfort measures (such as padding, warm blankets, and emotional support)
May assist with applying monitoring devices
Sets up suction and ensures that emergency equipment is readily available (defibrillator)

## Slide 38: Preoperative Routine
STSR
Greets patient and introduces self
Assesses patient to help them anticipate other items that may be needed for surgical procedure (if large patient, may need longer instruments)
Maintains a quiet environment to avoid causing added anxiety to the patient (do not test saws or clank your instruments)

## Slide 39: Intraoperative Routine
Position to:
Promote circulation and respirations
Prevent nerve, muscle strain, and pressure injury
When moving patient do so slowly for circulatory readjustment
Do not lean on the patient
Hearing is the last sense to go when being anesthetized!

## Slide 40: Post Anesthesia Care
CRNA/Anesthesiologist
Assists with transport to PACU or critical care unit
Primary responsibility during transport is to maintain the patient’s airway and ventilation
Gives verbal report to the nurse receiving the patient
Leaves area when patient is deemed stable to have their care be picked up by the PACU nurse

## Slide 41: Post Anesthesia Care
Circulator
Assists with transport of patient to the PACU or critical care unit
Locks stretcher or bed upon arrival to the PACU
Provides verbal report to the PACU nurse
Turns over care of patient to the PACU nurse

## Slide 42: Post Anesthesia Care
STSR
May assist with transfer of patient to the stretcher or unit bed
Should maintain their sterile field until it is certain that the patient is stable
Keep their surgical attire on so that they could change gown and gloves without re-scrubbing should the need arise to go back in
Transport their instrument cart to designated area after patient has left the OR room

## Slide 43: Post Anesthesia Care
Surgeon
Completes postoperative orders
May accompany patient to recovery area
Gives the patient’s family a verbal report
Discharges patient from the PACU when they are deemed stable and ready

## Slide 44: Summary
Anesthesia Concepts
Anesthesia Administration & Selection
Complications
Assisting During Anesthesia Administration