## Slide 1: Specialty Instrument Trays
Tracheotomy, Vascular, Chest
Plus
Large Self-Retaining Retractor Systems

## Slide 2: DON”T FREAK OUT!
Note the instruments that you have been learning are part of the Minor and Major Instrument Trays from AB-TECH and Mission Hospitals used in General Surgical and minor Procedures
You will find a few variations or “specialty” instruments with ALL SPECIALTY TRAYS
Focus on the variations as you learn these new trays

## Slide 3: “TRACH TRAY” Tracheotomy Tray
Tracheotomy- to make a “temporary” opening into the trachea
EXAMPLES:
Acute Head/Neck Trauma
Aspiration of foreign body
Trouble weaning off a ventilator
Tracheostomy- “permanent” opening into the trachea
EXAMPLES of Surgeries:
Total laryngectomy surgery for throat cancer/cancer of the larynx
Vocal Cord Surgery/Removal
Chronic Head/Neck Trauma
Chronic Ventilator Patient

## Slide 4: “TRACH TRAY” Instrument Variations
What you don’t know yet:
Trach hook
Trach spreaders

## Slide 5
Tracheotomy Tray

## Slide 6
The two instruments you didn’t recognize:
Trach Hook
(blunt tip)
Trach Spreader
“Three prong”
Also come two prong

## Slide 7: Peripheral Vascular (PV) Trays
I. Minor PV Tray
  Arteriovenous Fistula (AV Fistula)
  Embolectomy = removal of an embolus from a vessel
    Embolus is undissolved matter in the form of liquid, solid or gas
    Thrombectomy = removal of a thrombus from a vessel
    Thrombus is a blood clot
  Carotid Endarterectomy (CAE)
  Any MINOR vascular procedure

## Slide 8: Carotid Endarterectomy Instruments
Carotid Endarterectomy- Removal of atherosclerotic plaque from the carotid artery for carotid artery disease
FYI:
Arteriosclerosis = hardening of the arteries with age (we will all have this with age)
Atherosclerosis = blockage/plaque formation in an artery (affected by severity of arteriosclerosis)
Can endarterectomize ANY artery, however, the carotid is the most common one done to the long term positive outcome, unlike endarterectomies of other arteries.

## Slide 9: Carotid Tray/Instruments
What you don’t know yet: (See instrument book)
Peripheral vascular clamping and occluding instruments
Rummel/tourniquet keeper p. 152
Bulldog clamps
Freer elevator p. 112
#4 Penfield elevator p. 79
Nerve hook p. 157
Potts-smith (potts) scissors p. 152
Tenotomy scissors p. 152
Dietric forceps (are just fine debakey forceps)
Geralds or Potts forceps p. 157
Mills ring forceps p. 157
Castro-viejo needle holders p.151 (come delicate or heavy and short or longer)
4-12 Used in neuro and ophthalmic surgery as well

## Slide 10: Carotid Endarterectomy Instruments
Peripheral vascular clamping and occluding instruments:
Peripheral debakey clamps p. 147 instrument book
Right angle peripheral debakey clamp
*FYI peripheral debakeys come in different sizes as well
PDA (patent ductus arteriosis/coartation clamp/glassman) p. 148 instrument book
Fogarty hydrogrip clamps (take disposable inserts) p. 147 top
Bulldogs (see p.145 instrument book for examples of non-disposable variations)
Henley clamp
Martinez vascular clamp
Javid shunt clamp p. 146

## Slide 11: Peripheral Vascular Trays
Major PV Tray:
Femoral-Femoral Bypass Graft
Femoral-Popliteal Bypass Graft
Femoral-Tibial Bypass Graft
Axillo-Femoral Bypass Graft
AAA Repair (Abdominal Aortic Aneurysmectomy)
All of the above are done to correct a stenosis or obstruction somewhere along the flow of these arteries. Lower extremity arterial blood flow is compromised (ischemia), which compromises the limb involved (potential necrosis of limb). We “bypass” or re-route the blood flow to go around the obstruction or stenosis. Obstructions usually caused by atherosclerosis or trauma.
May also be used in conjunction with a “CHEST TRAY” for thoracic (lung) surgeries

## Slide 12: Peripheral Vascular Instruments
What you don’t know yet:
Peripheral debakey clamps
Satinsky clamps p. 149
Cooley clamps
Aortic clamps
Fogarty clamps
Fogarty bulldog spring applier p.146

## Slide 13
Alms retractor
Peripheral debakey clamp
Satinsky clamp
Potts-smith forceps
AKA Geralds
VASCULAR INSTRUMENTS

## Slide 14
Satinsky
VASCULAR CLAMPS
All vascular clamps have debakey lined jaws
and are considered clamping/occluding instruments
Peripheral Debakey
PDAs (patent ductus arteriosis)
Glovers/ Coarctation clamps
Angled and straight

## Slide 15
Potts-Smith scissors
or
Potts
Tips come 25º, 45º, 60º, and reverse
Also come in a castro style called “finger Potts”
Used for extending an arteriotomy or duct incision
Tenotomy scissors
See used to cut delicate tissue such as vessels, ducts, nerves

## Slide 16
Titanium “locking” Castro-Viejo Needle Holder
Also come non-locking
Come in a variety of finishes, lengths and jaw sizes
See used in Ophthalmic, Cardiovascular, peripheral vascular,
Neurosurgical and plastic surgeries
Jaws are smooth for gripping delicate suture needles
Should not use “fine tipped” castros on larger than 7-0 needle
To preserve tips

## Slide 17
Alms retractor
Garrett dilators
For dilating blood vessels
Vascular dilators

## Slide 18
Jackson Tunneler

## Slide 19: Chest Trays
Please note following instruments in your instrument book:
Pennington forceps p. 12 (the Pennington has a much smaller
than the Lovelace clamp but identical otherwise)
Duval or Lovelace Lung forceps p.150
Sarot bronchus clamp p. 150
Giertz-Shoemaker rib shears (Guillotine) p. 153
Doyan raspatory p. 154
Alexander raspatory p. 154
Bailey rib approximator p. 155
Allison lung retractor (wisk/egg-beater) p. 155
Tuffier rib spreader/retractor p. 156
Burford rib spreader/retractor p. 156
Davidson scapula retractor (p. 890 ST for the ST)

## Slide 20
Allison Lung Retractor

## Slide 21
Duval Lung Clamp

## Slide 22
Sarot Bronchus Clamp

## Slide 23
Davidson Scapular Retractor

## Slide 24
Rib Shears
Bethune
Giertz-shoemaker
aka:”guillotine”

## Slide 25
Bailey Rib Approximator

## Slide 26
Doyan Pig Tails
raspatories

## Slide 27
Periosteal elevators
Cameron
Alexander

## Slide 28
Finochietto Rib Retractor

## Slide 29: Large Self Retaining Retractor Systems

## Slide 30: Self-Retaining
Bookwalter Retractor
(Surgeon preference as there are others)
Self-Retaining abdominal retractor
Used with abdominal procedures
Table post
Rings x 2 (small & large)
Couplers for connection
Blades: Balfour, Richardson, Harrington, Malleables of various widths & lengths
Will hand up wet/wrung out lap with each blade passed for protection

## Slide 32: Omni-Tract
(Surgeon preference as there are others)
Self-Retaining abdominal retractor
Used with abdominal procedures
Table post
Arm
Couplers for connection
Blades one piece: Bladder blades, Richardson, Harrington, Malleables of various widths & lengths
Handles and screws for some of the three piece blades
Will hand up wet/wrung out lap with each blade passed for protection

## Slide 33
Omni-Tract
Heavy Castro-viejo
Needle holder